## Slide 1: Vishwakarma Application ID
VISHWAKARMA AWARDS 2026-27
VK26-IITH-SC-0172
Acoustic Canopy Pest Detection Collar (ACPDC)
An autonomous micro-acoustic bio-scouting array for early detection of sub-surface tree infestation
Track: Technological Innovation for Rural Sustainability

## Slide 2: Problem Context
25–30%
CROP LOSS MITIGATED (EST.)
80%
LESS CHEMICAL EXPOSURE (EST.)
≤48 h
TARGET DETECTION WINDOW
24/7
AUTONOMOUS MONITORING
Project overview
Title: ACPDC – clamp-on acoustic collar for boring-pest detection
Team ID: VK26-IITH-SC-0172
Track: Technological Innovation for Rural Sustainability
Core innovation: a piezo collar that hears larval boring at the edge and sends LoRa alerts per tree
Problem statement & beneficiaries
Boring larvae (Red Palm Weevil, Emerald Ash Borer) feed inside the trunk, invisible to drones, satellites and visual scouting until canopy collapse.
Result: reactive, calendar-based blanket spraying that pollutes water, kills beneficial insects, raises cost and breeds resistance.
Target users: commercial orchard owners, cooperative unions, forestry bureaus and biosecurity agencies.
Figures are Stage 1 proposal estimates; to be validated in Stage 3 field trials.

## Slide 3: User Journey: Before vs After
Before: reactive scouting
1. Larvae feed inside the trunk – no visible sign
2. Weeks later canopy chlorosis / wilt appears
3. Manual checks + blanket spraying of the whole orchard
4. Tree already lost; runoff, mortality, resistance
Detection only after vascular collapse
After: ACPDC autonomous pipeline
1. Collar listens on a duty-cycled schedule for larval boring impulses
2. Edge classifier flags sustained activity (≤48 h)
3. LoRa alert with tree ID reaches the dashboard
4. Targeted micro-injection on the flagged tree only
~80% less chemical exposure; 25–30% less crop loss (est.)

## Slide 4: System Architecture & Specs
Mechanical
clamp + Al plate
Sensing
PZT + analog AFE
Edge MCU
ADC, DSP, classifier
Telemetry
LoRa P2P 865 MHz
Receiver +
dashboard
Power: 6 V 1 W solar → CN3791 charger (NTC + protection) → NCR18650B → 3.3 V low-Iq regulator
Parameter | Target spec | Selected hardware / protocol
Sensing band | Bench-test A 1–14 kHz vs B 20–60 kHz | PZT-5H disc [P/N TBD], rigid Al-6061 contact
Analog front-end | 30 dB gain; LPF set per band | TLV9062S (shutdown); TLV9002S if low band
Sampling / DSP | 48 kS/s (A) vs 200 kS/s (B), 12-bit | STM32WLE5 (Cortex-M4) on Seeed Wio-E5
Power | ≤100 µA avg via scheduled capture | CN3791 + NCR18650B + 6 V 1 W solar
Telemetry | LoRa point-to-point, 865–867 MHz | Wio-E5 node → Wio-E5 Mini + laptop
Detection logic | Alert ≤48 h from onset | Adaptive threshold + N-of-M burst voting
Mechanical | IP67 (to be tested), <350 g | ASA housing, SS304 band, EPDM liner

## Slide 5: How the Collar Works (1/2): Hearing the Larva
Illustration of the sensing principle (not to scale)
1
Larva boring makes vibration
Feeding larvae chew inside the trunk, producing short impulsive clicks that travel through the wood.
2
Rigid contact picks it up
The Al-6061 plate presses the PZT disc onto the trunk; vibration becomes a tiny voltage. No rubber in this path.
3
Front end conditions the signal
TLV9062S adds ~30 dB gain; a per-band low-pass filter feeds the ADC. Band is set after bench tests.

## Slide 6: How the Collar Works (2/2): From Sound to Alert
Signal path inside the collar (synthetic, illustrative)
Alert path from collar to dashboard (illustrative)
1
Wake & capture
Duty-cycled: MCU wakes, powers the AFE and records a short burst.
2
Filter & vote
Band-pass plus adaptive threshold and N-of-M voting reject wind and rain.
3
Send LoRa alert
Tree ID goes out over LoRa P2P with ack + retry; target alert ≤48 h.
4
Treat that tree
Dashboard flags the tree, so spraying is targeted, not blanket.

## Slide 7: CAD Design & Mechanical Specs
ACPDC collar CAD model (STL export): isometric and top view
Material selection
Housing: ASA (UV-stable) over PETG/PC; light grey limits solar heating
Sensing path: Al 6061-T6 plate in rigid, direct trunk contact; no rubber between plate and bark
Clamp: SS304 band + spring tensioner (no girdling); EPDM only isolates housing and clamp
FEA / stress plan
Load cases: clamp preload, wind drag, 70 °C thermal soak
Hand calc: wind drag ≈ 7 N at 40 m/s (Cd 1.2, A 0.006 m²); mount FoS target ≥ 3

## Slide 8: Electronics Signal Chain & BOM
PZT-5H disc
Ø12 mm
Pre-amp
TLV9062S ×31
Anti-alias LPF
set per band
ADC + DMA
48 / 200 kS/s
IIR band-pass
+ N-of-M vote
LoRa P2P TX
865–867 MHz
Component | Part / specification | Qty | Lead time | Est. cost
LoRa node module | Seeed Wio-E5 bare module (STM32WLE5JC) | 3 | Imported, 10–14 d | ₹3,186
LoRa dev + receiver | Seeed Wio-E5 Mini dev board | 2 | Imported, 10–14 d | ₹5,184
Piezo sensor | PZT-5H disc Ø12 mm [ADD mfr P/N] | 6 | Local, 5 d | ₹900
Analog front-end | TLV9062S ×6 + FR4 2-layer PCB ×5 | — | Local, 7 d | ₹2,340
Charger & protection | CN3791 module, NTC, Li-ion protection, 3.3 V reg | 3 sets | Local, 3–5 d | ₹1,272
Cell & solar | NCR18650B (genuine) + 6 V 1 W panel | 3 sets | Local, 5 d | ₹2,100
Enclosure | IP67 gasketed enclosure + printed bracket (quote) | 3 | Local, 5 d | ₹2,100
Clamp & coupling | Al-6061 plate, SS304 band, EPDM liner | 3 | Local, 7 d | ₹1,800
Misc. | Connectors, passives, wire, coating | lot | Local, 3 d | ₹1,500
Total (3 nodes + receiver) |  |  |  | ₹20,382
.

## Slide 9: Your Maker Journey
Authenticity verification
Collaborating on the design and development of the ACPDC project
Raw repository linkage
https://github.com/tobiocat/ACPDC
*https://1drv.ms/p/c/2e7b3fc7bcb40db0/IQC7Q1St8HDHTrJO5VEVXUEjAaHzmrqYc0-vIMAZ9zX0f5I?e=F90D15*

## Slide 10: Safety & Hazard Mitigation
Failure mode | Effect | Embedded fail-safe
Wind / rain / vehicle noise | False alarm, needless treatment | Band-pass + N-of-M burst voting; broadband-burst rejection
Loose clamp / detached sensor | Missed detection | Daily coupling self-test; alert on fail
Battery under-voltage / cold | Brown-out, cell damage | Protection-board UV cutoff; NTC charge inhibit <0 °C; low-battery beacon
LoRa link loss | Alert never arrives | Flash store-and-forward; ack + retry; 24 h heartbeat
Firmware hang | Silent node | Hardware watchdog reset + OTA rollback image
Physical fail-safes
IP67 gasketed enclosure + vent
PTC fuse + reverse-polarity guard
Non-girdling spring tensioner
Rounded edges, no exposed live parts
Standards (design targets)
IEC 60529 (IP67, tested on final unit)
IEC 62133-2 / IS 16046, UN 38.3 (Li-ion)
WPC ETA for 865–867 MHz LoRa
IEC 61000-4-2 ESD, CISPR 32
ASTM G154 UV (ASA housing)

## Slide 11: Roadmap: 4-Month Fabrication Plan
Nov 2026: Fabricate
Band test on wood: 48 vs 200 kS/s
Coupling test: rigid vs rubber contact
Freeze KiCad schematic + CAD
Dec 2026: Assemble & bring-up
Fab PCBs; populate and test AFE
Measure bare-module current (no devkit LEDs/USB)
ADC-DMA capture + band-pass firmware
Jan 2027: Integrate
LoRa P2P link to laptop receiver
Adaptive-threshold classifier
Dashboard MVP; bench test on wood
Feb 2027: Validate
3-node orchard trial
Log false alarms; tune clamp + power
Stage 3 demo prep
Stage 3 commitment: a working 3-node prototype with laptop receiver demonstrating live acoustic detection → LoRa alert → dashboard, with bench and orchard detection / false-alarm logs.

## Slide 12: Technical Challenges & Risks
1. Unproven band + ambient noise
A published RPW study found features near 2–14 kHz; 20–60 kHz may miss signal
Wind, rain and traffic set the false-alarm rate
2. Coupling and attenuation in wood
Species, bark, moisture and clamp force change sensitivity
High-frequency energy fades quickly along the trunk
Rubber in the sensing path weakens the signal
3. Power vs continuous operation
TLV9062 draws ~538 µA per channel (~1.1 mA per IC)
Reaching ≤100 µA needs scheduled capture + shutdown
4. Ground truth and permits
Live quarantine pests are tightly regulated
Few labelled larval recordings to train the classifier

## Slide 13: Potential Solutions & Risk Mitigation
Risk | Primary mitigation | Backup / fallback
Band & noise | Bench-compare 1–14 kHz @48 kS/s vs 20–60 kHz @200 kS/s; N-of-M voting | Dual-band firmware, OTA-selectable; TinyML classifier
Coupling | Rigid Al-plate contact; rubber only on housing/clamp | Coupling gel; per-tree baseline; coupling test
Attenuation | Mount on main trunk; node density by tree size | Second collar on limbs
Power budget | Scheduled capture; TLV9062S shutdown between recordings | TLV9002S (~60 µA/ch) if low band works
Data and permits | Piezo exciter on wood + public recordings | Partner with a state research station for live samples
Link loss | Elevated antenna; ack + retry; flash store-and-forward | Add LoRaWAN gateway for scale-up

## Slide 14: References & Sources
ACPDC Stage 1 Project Proposal, Vishwakarma Award submission (Sept 2026)
Source: internal
STM32WLE5 datasheet; Seeed Wio-E5 module documentation
Source: www.st.com, www.seeedstudio.com
TLV9062 and TLV9002 datasheets
Source: www.ti.com
USDA-ARS red palm weevil acoustic detection study (2–14 kHz features)
Source: www.ars.usda.gov
IEC 60529 (IP codes); IEC 62133-2 (Li-ion cells)
Source: webstore.iec.ch
Diagrams in this deck are original illustrations; no third-party images used
Peer-reviewed literature: acoustic detection of boring larvae (RPW / EAB)
Larval bursts are broadband (1–20 kHz); background noise peaks below ~3.5 kHz [1]. Burst and pulse-rate rules detect larvae [3, 4].
[1] Mankin RW, Al-Ayedh HY, Aldryhim Y, Rohde B (2016) Acoustic detection of Rhynchophorus ferrugineus and Oryctes elegans in Phoenix dactylifera trees and offshoots in Saudi Arabian orchards. J. Econ. Entomol. 109(2): 622–628. doi:10.1093/jee/tov398
[2] Herrick NJ, Mankin RW (2012) Acoustical detection of early instar Rhynchophorus ferrugineus in Canary Island date palm, Phoenix canariensis. Fla. Entomol. 95(4): 983–990. doi:10.1653/024.095.0425
[3] Mankin RW, Mizrach A, Hetzroni A, Levsky S, Nakache Y, Soroker V (2008) Temporal and spectral features of sounds of wood-boring beetle larvae: identifiable patterns of activity enable improved discrimination from background noise. Fla. Entomol. 91: 241–247